## Slide 1: Hierarchical Trust Management for Wireless Sensor Networks and its Applications to Trust-Based Routing and Intrusion Detection
Presented by:
Vijay Kumar Chalasani

## Slide 2: Introduction
This paper proposes “hierarchical trust management protocol”
Key design issues
  Trust composition
  Trust aggregation
  Trust formation
Highlights of the scheme
  Considers QoS trust and social trust
  Dynamic learning
  Validation of objective trust against subjective trust
  Application level trust management

## Slide 3: System Model
Cluster based WSN (wireless sensor network)
SN  CH  base station or sink or destination
Two level hierarchy
  SN level
  CH level
At SN level
  Periodic peer to peer trust evaluation with an interval Δt
  Send SNi-SNj trust evaluation result to CH

## Slide 4: System Model
At CH level
  Send CHi-CHj trust evaluation result to base station
  Evaluate CH – SN trust towards all SNs in the cluster
Trust metric
  Social trust : intimacy, honesty, privacy, centrality, connectivity
  QoS trust : competence, cooperativeness, reliability, task completion capability, etc.
In this paper, intimacy and honesty are chosen to measure social trust. Energy and unselfishness are chosen to measure QoS trust.

## Slide 5: Hierarchical Trust Management Protocol
Two levels of trust : SN level and CH level
Evaluations through
  Direct observations
  Indirect observations
Trust components : intimacy, honesty, energy, and unselfishness
Tij = w1Tijintimacy (t) + w2Tijhonesty (t)
+w3Tijenergy (t) + w4Tijunselfishness (t)
w1+w2+w3+w4 = 1

## Slide 6: Hierarchical Trust Management Protocol (cont.)
Peer to Peer Trust evaluation
  For 1-hop neighbors
  TijX (t)= (1-α) TijX (t- Δt) + α TijX,direct
  = trust based on past experiences + new
  trust based on direct observations
  (0 ≤ α ≤ 1) (decay of trust)
  Otherwise
  TijX = avgk∈Ni {(1-ϒ) TijX (t- Δt) + ϒTkjX,recom (t) }

## Slide 7: Obtaining trust component value TijX,direct for 1-hop neighbors
Tijintimacy, direct (t) :
  Ratio of # of interactions between i and j in (0, t) & # of interactions between i and any other node in (0, t)
Tijhonesty, direct (t) :
  Measured based on count of suspicious dishonest experiences
  ‘0’ when node j is dishonest
  1-ratio of count to threshold

## Slide 8: Obtaining trust component value TijX,direct for 1-hop neighbors
Tijenergy, direct (t) :
  By keeping track of j’s remaining energy
Tijunselfishness, direct (t) :
  By keeping track of j’s selfish behaviour

## Slide 9: Obtaining trust component values for the nodes that are not 1-hop neighbors
TijX (t)=avgk∈Ni {(1-ϒ) TijX (t- Δt) + ϒTkjX,recom (t) }
  Past experiences + recommendations of 1-hop neighbors
  ϒ = ………..trust decay over time
  is node i’s trust over k as recommender
  , specifies the impact of indirect recommendations

## Slide 10: Trust Evaluations
CH to SN trust evaluation:
  If Tcj (t) less than Tth , then node j is compromised else j is not compromised
  CH also determines from whom to take trust recommendations
Station to CH trust evaluation:
  Same fashion as of the above evaluation

## Slide 11: Performance Model
Probability model based on SPN
  Obtain objective trust
ENERGY
  Indicates the remaining energy level
T_ENERGY
  Rate of transition T_ENERGY is energy consumption rate
Energy

## Slide 12: Performance Model
Selfishness
T_SELFISH T_REDEMP
P selfish = µ + (1- µ)
  Transition rates
  T_SELFISH = P selfish / Δt
  T_REDEMP = (1 - P selfish ) / Δt
SN

## Slide 13: Performance Model
Compromise
T_COMPRO
T_IDS
rate of T_COMPRO , λ = λc-init (#compromised 1-hop neighbors/#uncompromised 1-hop neighbors)
CN
DCN

## Slide 14: Subjective trust evaluation
  TijX,direct (t) is close to actual status of node j at time t
  Tijhonesty,direct (t):
    Status value of ‘0’ if j is compromised in that state. Else ‘1’
  Tijenergy,direct(t) :
    Status value of Energy/Einit
  Tijunselfishness,direct(t) :
    Status value of ‘0’ if j is selfish in that state. Else ‘1’

## Slide 15: Subjective Trust evaluation
  Tijintimacy,direct(t) :
    Is not directly available from state representations
    Calculated based on interactions like : Requesting, Reply, Selection, Overhearing
    If a, b, c are average # interactions with selfish node, compromised node , normal node respectively
    a = 25% * 50% *3 + 25% *2 + 25% *2
    b = 0 + 25% *2
    c = 25% *3 + 25% *2
    Status value a/c is given to states in which j is selfish. status value b/c is given to states in which j is compromised and c/c (1) to states where j is normal

## Slide 16: Objective trust evaluation
Objective trust is computed based on the actual status as provided by the SPN model
Tj,obj(t) = w1Tj,objintimacy (t) + w2Tj,objhonesty (t)
+w3Tj,objenergy (t) + w4Tj,objunselfishness (t)
The objective trust components reflect node j’s ground truth status at time t

## Slide 17: Trust Evaluation Results
Here, graph is plotted for X = intimacy
As α increases, sbj trust approaches obj trust initially. But deviates after cross over
As β increases, sbj trust approaches obj trust initially. But deviates more after cross over
best α, β values depend on nature of each trust property and given set of parameter values.

## Slide 18: Trust Based Geographic Routing
Geographic Routing: A node disseminates a message to L neighbors closest to the destination
In trust based Geographic routing, not only closeness but also trust values are taken into account

## Slide 19: Trust Based Geographic Routing
Assuming weights assigned to social trust properties are same (similar assumption to Qos trust)
Balance between Wsocial & WQoS
It can dynamically adjust Wsocial to optimize application performance

## Slide 20: Trust Based Geographic Routing: performance comparison
Delay increases with increase of compromised nodes
Message delay in GR is less than Message delay in Trust based GR
Trust base GR has more message overhead as compared to traditional GR
# messages propagated = 3 when compromised or selfish nodes are >80%

## Slide 21: Trust Based Intrusion Detection
Based on the idea of minimum trust threshold
CH evaluates a SN with the help of trust evaluations received from the other SNs
Considering trust value towards node j a random variable
(n sample values of Tij(t) are provided by n SNs)
, ), and are sample mean, sample standard deviation, and true mean respectively

## Slide 22: Trust Based Intrusion Detection
Prob of j being diagnosed as compromised
Θj(t) = Pr( < Tth)
= Pr()
False negative prob:
Pjfn = Pr()
False positive prob:
Pjfp = Pr()
Average values over time:
Pjfp=
Pjfn=

## Slide 23: Trust Based Intrusion Detection: Comparisons

## Slide 24: Conclusion
Approach considered two aspects of trustworthiness : Social and QoS
Made use of SPN to analyze and validate protocol performance
Comparisons are made with other techniques