## Slide 1: Object Placement for High Bandwidth Memory Augmented with High Capacity Memory
Mohammad Laghari and Didem Unat
SBAC-PAD 2017 @ Campinas, Brazil 17-20 October 2017
https://parcorelab.ku.edu.tr

## Slide 2: Introduction
Image taken from: http://www.amd.com/en/technologies/hbm
To overcome memory bandwidth limitations, multiple memories with different characteristics are introduced
Data locality for applications on heterogeneous memory systems (High Bandwidth Memory + High Capacity Memory)
High Bandwidth Memory (HBM)
  High bandwidth
  Limited capacity
  3D structure (connected with TSVs)
  Expensive (due to technology limitations)
  Eg. MCDRAM on Intel Knights Landing
High Capacity Memory (HCM)
  Low bandwidth
  Huge capacity
  Eg. DDR
Notes: The question arises of how to intelligently place data on such systems such that the overall application performance is maximized.

## Slide 3: Data Placement on HBM
Only single memory type
Place data on HCM
HCM
CPU
HBM
?
?
How to allocate objects in systems with multiple memory types
Memories have different properties

## Slide 4: Data Placement on HBM
HCM
CPU
HBM
?
?
Part of the HBM acts as the Last Level Cache (hardware prefetching)
Cache

## Slide 5: Intel Knights Landing (KNL) overview
MCDRAM
MCDRAM
MCDRAM
MCDRAM
MCDRAM
MCDRAM
MCDRAM
MCDRAM
misc.
PCIe Gen. 3
DMI
DDR MC
DDR MC
3
DDR4
Channels
EDC
EDC
EDC
EDC
EDC
EDC
EDC
EDC
3
DDR4
Channels
Up to 36 Tiles connected by 2D interconnect mesh
Shared 1MB L2
Core
Core
2 VPUs
2 VPUs
Cache/Home Agent
2 cores per tile
8 High Bandwidth Memory modules (2 GB each)
8 access channels to HBM
6 access channels to HCM
Notes: Selfboot: no PCIe bottleneck
Binary compatibility: runs legacy code, unlike KNC, no recompilation
Improved vector density: 3+ Tflops DP, 6+ Tflops SP

## Slide 6: Intel KNL Overview – cont.
Intel KNL Memory Modes
Flat Mode
DDR
HBM as 16GB L3 Cache
DDR
HBM as 16GB addressable
DDR
HBM as 4GB L3 Cache
HBM as addressable 12 GB
Cache Mode
Hybrid Mode
HBM is separately addressable
HBM acts as a hardware managed cache
HBM acts as a combination of Flat and Cache mode
Notes: Selfboot: no PCIe bottleneck
Binary compatibility: runs legacy code, unlike KNC, no recompilation
Improved vector density: 3+ Tflops DP, 6+ Tflops SP
All-to-All: memory addresses are uniformly distributed across all TDs on the chip
Quadrant: Memory addresses served by a memory controller in a quadrant are guaranteed to be mapped only to TDs contained in that quadrant
SNC:

## Slide 7: Placement Algorithm
Placement is suggested by our variation 0-1 Knapsack dynamic algorithm
  We don’t break the object (whole object is placed on one of the memory types)
Item Size: Object Size
Item Value: Object reference Count
E
D
A
B
C
F
Knapsack Size: HBM Size
HBM
Size: 10
Value: 20
Size: 50
Value: 10
Size: 5
Value: 200
Size: 50
Value: 40
Size: 10
Value: 50
Size: 8
Value: 20

## Slide 8: Memory Benchmarks
Perform benchmarking of Intel MCDRAM (HBM) to find out its performance capabilities
We used well-known Stream benchmark
  Problem size
    Array size = 80M elements
    Total memory required = 1.8 GB
  KNL configuration
    SNC4 + Flat
    64 cores (not 68)
  Execution
    KMP_AFFINITY=scatter

## Slide 9: Stream Benchmark
A[i] = B[i] + α*C[i]

## Slide 10: Stream Benchmark
MCDRAM peak tested bandwidth: 450+ GB/s
DDR peak tested bandwidth: 85+ GB/s
A[i] = B[i] + α*C[i]

## Slide 11: Bandwidth Studies on HBM
Chart: 
| 8 | 16 | 32 | 64 | 128 | 256
All-DDR | 68.0031 | 85.2122 | 86.5521 | 86.4981 | 83.4817 | 68.4272
All-MCDRAM | 59.5143 | 123.8952 | 235.5799 | 425.9162 | 445.3079 | 435.3285
DDR(a,b) , MCDRAM(c) | 59.6108 | 83.8721 | 85.2654 | 84.2732 | 83.9595 | 81.5426
DDR(b,c) , MCDRAM(a) | 60.6291 | 116.3788 | 124.846 | 122.7152 | 125.2109 | 121.4109
DDR(c) , MCDRAM(a,b) | 62.4346 | 122.9044 | 212.2467 | 223.4107 | 232.4989 | 225.5065
DDR(a) , MCDRAM(b, c) | 62.0837 | 113.8451 | 119.798 | 121.3652 | 120.5657 | 118.087
Number of threads
Bandwidth (GB/s)
Memkind: release version 1.6.0
A[i] = B[i] + α*C[i]

## Slide 12: Bandwidth Studies on HBM
Chart: 
| 8 | 16 | 32 | 64 | 128 | 256
All-DDR | 68.0031 | 85.2122 | 86.5521 | 86.4981 | 83.4817 | 68.4272
All-MCDRAM | 59.5143 | 123.8952 | 235.5799 | 425.9162 | 445.3079 | 435.3285
DDR(a,b) , MCDRAM(c) | 59.6108 | 83.8721 | 85.2654 | 84.2732 | 83.9595 | 81.5426
DDR(b,c) , MCDRAM(a) | 60.6291 | 116.3788 | 124.846 | 122.7152 | 125.2109 | 121.4109
DDR(c) , MCDRAM(a,b) | 62.4346 | 122.9044 | 212.2467 | 223.4107 | 232.4989 | 225.5065
DDR(a) , MCDRAM(b, c) | 62.0837 | 113.8451 | 119.798 | 121.3652 | 120.5657 | 118.087
Number of threads
Bandwidth (GB/s)
Memkind: release version 1.6.0
A[i] = B[i] + α*C[i]

## Slide 13: Bandwidth Studies on HBM
Chart: 
| 8 | 16 | 32 | 64 | 128 | 256
All-DDR | 68.0031 | 85.2122 | 86.5521 | 86.4981 | 83.4817 | 68.4272
All-MCDRAM | 59.5143 | 123.8952 | 235.5799 | 425.9162 | 445.3079 | 435.3285
DDR(a,b) , MCDRAM(c) | 59.6108 | 83.8721 | 85.2654 | 84.2732 | 83.9595 | 81.5426
DDR(b,c) , MCDRAM(a) | 60.6291 | 116.3788 | 124.846 | 122.7152 | 125.2109 | 121.4109
DDR(c) , MCDRAM(a,b) | 62.4346 | 122.9044 | 212.2467 | 223.4107 | 232.4989 | 225.5065
DDR(a) , MCDRAM(b, c) | 62.0837 | 113.8451 | 119.798 | 121.3652 | 120.5657 | 118.087
Number of threads
Bandwidth (GB/s)
Memkind: release version 1.6.0
A[i] = B[i] + α*C[i]

## Slide 14: Bandwidth Studies on HBM
Chart: 
| 8 | 16 | 32 | 64 | 128 | 256
All-DDR | 68.0031 | 85.2122 | 86.5521 | 86.4981 | 83.4817 | 68.4272
All-MCDRAM | 59.5143 | 123.8952 | 235.5799 | 425.9162 | 445.3079 | 435.3285
DDR(a,b) , MCDRAM(c) | 59.6108 | 83.8721 | 85.2654 | 84.2732 | 83.9595 | 81.5426
DDR(b,c) , MCDRAM(a) | 60.6291 | 116.3788 | 124.846 | 122.7152 | 125.2109 | 121.4109
DDR(c) , MCDRAM(a,b) | 62.4346 | 122.9044 | 212.2467 | 223.4107 | 232.4989 | 225.5065
DDR(a) , MCDRAM(b, c) | 62.0837 | 113.8451 | 119.798 | 121.3652 | 120.5657 | 118.087
Number of threads
Bandwidth (GB/s)
Memkind: release version 1.6.0
A[i] = B[i] + α*C[i]

## Slide 15: Bandwidth Studies on HBM
Notes: In this section we investigate the read and write bandwidths of MCDRAM and DDR. The experiments show MCDRAM bandwidth of 350 GB/s and 270 GB/s for read and write, respectively. It seems that up to 32 cores, the benchmark is not bandwidth-limited on MCDRAM. In general write operations have slightly less overhead than reads in terms of data movement. The higher cost of write at the memory controller or in the memory shows up only when the application becomes bandwidth-limited. We see this trend on MCDRAM up to 32 cores, when the write performance is better than read. Bandwidth on DDR is more stable with varying number of threads, 88 GB/s and 50 GB/s for reads and writes, respectively.

## Slide 16: Bandwidth Studies on HBM
Generally write bandwidth is lower on both memories
Notes: In this section we investigate the read and write bandwidths of MCDRAM and DDR. The experiments show MCDRAM bandwidth of 350 GB/s and 270 GB/s for read and write, respectively. It seems that up to 32 cores, the benchmark is not bandwidth-limited on MCDRAM. In general write operations have slightly less overhead than reads in terms of data movement. The higher cost of write at the memory controller or in the memory shows up only when the application becomes bandwidth-limited. We see this trend on MCDRAM up to 32 cores, when the write performance is better than read. Bandwidth on DDR is more stable with varying number of threads, 88 GB/s and 50 GB/s for reads and writes, respectively.

## Slide 17: Placement Algorithm
MCDRAMWRITE_BW > DDRWRITE_BW , so place write-intensive data on MCDRAM?
Application performance limited to DDRWRITE_BW
Two flavors of the placement algorithm
  Write Agnostic:
    Does not differentiate between reads and writes
  Write Sensitive:
    Considers write accesses different from the reads
    MCDRAM on Intel KNL has varying Read/Write bandwidths
    We prioritize writes with a factor of 1.5 over reads

## Slide 18: Placement Algorithm – cont.
Typical knapsack algorithm returns the candidate object list for HBM.
Added a coefficient α to prioritize writes over read references
We used α= 1.5 for KNL.

## Slide 19: Obtaining Object Reference Counts
Tried Intel Pin Tool
Provides object memory access trace for an application
Slows down application runtime by a factor of 100
Advanced DAta Movement ANalysis Toolkit: ADAMANT (v2.0)
Provides object level statistics including references to objects
Statistics are based on sampled events
Obtain Reference Counts using ADAMANT
Find placement strategies using the Our Placement Algorithm
Apply placement strategies by allocating objects to suggested memory types
Notes: Adamant: sampling
Pintool: complete profile, can be slow

## Slide 20: Evaluation of Placement Algorithm

## Slide 21: Applications Used
Applications | Description | # of Objects | Footprint (GB)
Triad | Triad kernel of STREAM benchmark | 3 | 6.00
Matrix Transpose | Transpose of a matrix is stored in another matrix | 2 | 6.00
Conjugate Gradient (CG) | Conjugate Gradient solves unstructured sparse linear systems | 13 | 5.23
HotSpot | Approximates processor temperature and power by solving PDEs | 3 | 6.00
Image Segmentation | Divides and recolors an image into segments to identify boundaries | 7 | 5.55
Breadth-First Search (BFS) | Breath first search graph traversal algorithm | 6 | 9.74

## Slide 22: Comparing with All-DDR or ALL-MCDRAM
All application data in DDR
All application data in MCDRAM
Application data divided between DDR and MCDRAM
Our placement
(without the presence of cache)
All configurations have a Flat Memory configurations i.e. Code modification is required
DDR
CPU
MCDRAM
DDR
CPU
MCDRAM
DDR
CPU
MCDRAM

## Slide 23: Comparing with All-DDR or ALL-MCDRAM
We achieve up to 2.5x speedup over All-DDR using placement suggested by our algorithm only using 4GB of HBM

## Slide 24: Comparing with All-DDR or ALL-MCDRAM
Matrix Transpose shows the effect of the MCDRAM latency.
Applications such as BFS do not perform well because of their latency sensitive nature (MCDRAM has a higher latency than DDR)
Notes: BFS and Matrix transpose: Irregular accesses, MCDRAM high latency
Matrix Transpose: Strided Access effect

## Slide 25: Comparing with 4GB Cache
Application data divided between DDR and MCDRAM
All application data in DDR, MCDRAM acting as Cache (4GB)
DDR
CPU
MCDRAM
DDR
MCDRAM as 4GB Cache
CPU
MCDRAM as Cache allows hardware prefetching i.e. no code modifications
Our placement
(without the presence of cache)

## Slide 26: Comparing with 4GB Cache
Our placement vs 4GB cache in Cache Mode (automatic hardware prefetching with no modifications to the source code)

## Slide 27: Placement augmented with some cache
Our placement (with cache)
All application data in DDR and MCDRAM acting as Cache (8GB)
Application data divided between DDR and MCDRAM (12 GB)
DDR
MCDRAM as 8GB Cache
MCDRAM as Cache allows hardware prefetching i.e. no code modifications
CPU
DDR
MCDRAM as 8GB Cache
CPU
MCDRAM

## Slide 28: Placement augmented with some cache
Our placement (+4GB Cache) vs 8GB cache in Cache Mode (automatic hardware prefetching with no modifications to the source code)

## Slide 29: Summary and Future Work
Our object placement algorithm
  Chooses the right objects in the case HBM capacity is not sufficient to hold all objects
  Performs better than when HBM is used as a cache
Other observations
  Accessing objects placed in different memory types in the same loop does not seem to be a good idea
  Write-sensitive placement is better because of the low write bandwidth of DDR
  Latency sensitive applications enjoy cache and prefers DDR
Future Work
  Conduct experiments on more complex applications with varying number of threads
  Automate the placement of objects

## Slide 30: Thank you
This project is supported by TUBITAK with project number 116C066. Authors from Koç University are supported by TUBITAK Grant No: 215E185. Authors would like to thank Dr. Pietro Cicotti from San Diego Supercomputer Center for his input in project
ParCore Lab @ Koç University
Istanbul, Turkey
https://parcorelab.ku.edu.tr

## Slide 31: Extra Slides

## Slide 32: High Bandwidth Memory (HBM)
HBM consists of DRAM stacked on top of each other
  3D structure of DRAMs
  Can be housed on the same package as the chip
HBM on Intel Knights Landing (KNL)
  Capacity vs Stream Bandwidth
    MCDRAM: 16 GB and 450 GB/s
    DDR4: 384 GB and 85 GB/s
    Latency of MCDRAM is slightly higher than DDR4
  Configurable at boot
    Flat Mode
    Cache Mode
    Hybrid Mode
Image taken from: http://www.amd.com/en/technologies/hbm
Notes:   MCDRAM: 150 ns
  DDR4: 125 ns

## Slide 33: Data Placement on HBM
Memkind library (latest release 1.6.0) or hbwmalloc library
Provides interface for explicit allocation on HBM
Double *a = (double *)malloc(sizeof(double) * 100)
Double *a = memkind_malloc(MEMKIND_DEFAULT, sizeof(double)*100)
OR
Double *a;
memkind_posix_memalign(MEMKIND_INTERLEAVE, &(void*)a, 1024, sizeof(double)* 100)

## Slide 34: Experiment Configurations
 | Fast Memory | Slow Memory | Cache (L3) | Boot Mode
All-DDR | --- | 384GB | --- | Flat
All-MCDRAM | 16GB | --- | --- | Flat
4GB Cache | --- | 384GB | 4GB | Hybrid
8GB Cache | --- | 384GB | 8GB | Hybrid
Our Placement (w/o Cache) | 4GB | 384GB | --- | Flat
Our Placement (w/ Cache) | 4GB | 384GB | 4GB | Hybrid
(64 Cores with Sub-NUMA 4 Clustering Mode)

## Slide 35: Memory Copy

## Slide 36: Memory Copy
Peak MCDRAM bandwidth achieved is 165 GB/s because read operation from DDR becomes a bottleneck

## Slide 37: Experimental Setup
Intel KNL equipped with 68 cores
Sub-NUMA 4 clustering mode
Scattered thread affinity
4GB of MCDRAM used as maximum (unless stated otherwise)
384GB of DDR

## Slide 38: Optimization Notes
Streaming stores is set to bypass cache for writes
  -qopt-streaming-stores always
Vectorization flag is set
  -Xmic-AVX512
Aligned memory during allocation
  memkind_posix_memalign()
Big pages (2MB)
  Got allocation error with hbw_*
Compilation report is checked if everything is expected
  -qopt-report5
Experimented with different OpenMP schedule chunksize
  Best is not to specify a chunksize

## Slide 39: Overall picture
Understanding the application characteristics
Analyze application read-write pattern by ADAMANT tool
Run our algorithm
Allocate objects on the memory suggested by the placement algorithm

## Slide 40: HotSpot with varying thread count